## Slide 1: What MSEEL Tells us about shale gas water and waste
Paul Ziemkiewicz, PhD, Director
West Virginia Water Research Institute
West Virginia University
Academic Media Day
Morgantown WV
11 Oct 16

## Slide 2
Marcellus Shale Energy and Environment Laboratory
MSEEL
Notes: TITLE: The Marcellus Shale Energy and Environment Laboratory (MSEEL)
The Marcellus Shale Energy and Environment Laboratory (MSEEL) consists of a multidisciplinary and multi-institutional team undertaking integrated geoscience, engineering and social science research in cooperation in cooperation with the operator, Northeast Natural Energy, numerous industrial partners and the National Energy Technology Laboratory of the US Department of Energy. MSEEL consists of two legacy horizontal production wells, two new instrumented horizontal production wells, a vertical pilot bore-hole, a microseismic observation well and surface geophysical and environmental monitoring stations. Production from the new horizontal well began in December 2015. The goal is to develop and validate new knowledge and technology that can improve recovery efficiency and minimize environmental impacts of unconventional resource development. The MSEEL approach is data driven with a platform to store, manage, publish and share very large and diverse (multiple terabyte) datasets among researchers. MSEEL integrates drilling and fracture stimulation operations, geophysical observations, fiber-optic monitoring of high-resolution temporal and spatial flow of injected and produced fluids, and produced gases, mechanical properties logs, microseismic and core data to better to characterize subsurface rock properties, faults and fracture systems. Models at multiple scales are being developed to identify best practices for field implementation, and assess potential methods that could enhance shale gas recovery through experimental and numerical studies integrated with the detailed results of the production wells at the MSEEL site. We provide several examples that illustrate technologies and approaches that are being developed to store, query, and display and analyze large and diverse data sources and new data types derived from surface and subsurface to design innovative stage spacing and cluster density practices that can be used to optimize recovery efficiency.

## Slide 3: MSEEL Drilling MIP 3H and 5H

## Slide 4: MSEEL Completion MIP 3H and 5H

## Slide 5: Water and solid waste studies: Characterization and management
Water
Hydrofrac fluids
Makeup water
Flowback
Produced water
Solid wastes
Drill cuttings
Mud

## Slide 6: Producing Marcellus well pad: 4 wells
2 hectares total
access/service road
out slopes
1.2 hectares pad
well heads
separators
condensate tanks

## Slide 7: Producing well site with impoundment
6 hectares:
access/service road
well heads
separators
condensate tanks

## Slide 8: Fluids at the well site

## Slide 9: Produced water volumes: MIP 3,5H after160 days 3H produced 92% more water, 30% more gas 1 bbl=0.16 m3 6.25 bbl/m3
~10% of injected water
4675 bbl

## Slide 10: Chemical Characterization
Flowback/produced water
  Sampled at upstream end of seperators
Hydraulic fracturing fluid
Drilling mud

## Slide 11: Produced water evolution: MIP 3H
Makeup-Mon River
TDS: 285 mg/L
Flowback day 0
TDS: 27,812 mg/L
Flowback day 160
TDS: 121,536 mg/L
30 days post completion

## Slide 12: Nearly all parameters were higher in flowback than frac fluid MW=makeup water HF=frac fluid MIP=produced water

## Slide 13: MW: Makeup water, HF: Hydraulic fracturing fluid, MIP: produced water

## Slide 14: Terminology: solid wastes
Drilling mud
  Returns to the surface with cuttings during drilling
  Recycled after cuttings removed
  To disposal after well completed
Drill cuttings
  Rock fragments-clay to fine gravel
  ~500-800 tons/well or 25 to 50 truckloads
  To disposal after separation from drilling mud
Flowback Solids-filter cake, precipitates, suspended solids

## Slide 15: Drilling wastes
Mud
Cuttings

## Slide 16: Solids separation
Cuttings pit
Flowback pit
Plate and frame filter press
Bag filters
Flowback tanks

## Slide 17: Conventional drilling mud Drill Cuttings % samples (Liquid fraction) > TCLP limit

## Slide 18: Using ‘Green’ Drilling Mud no parameters exceeded TCLP
In the Vertical and Horizontal (Marcellus) sections:
  TCLP organics-no exceedances
  TCLP inorganics-no exceedances

## Slide 19: Drilling mud: Bio-Basetm 365
Property Unit Value Test Method
Physical state Liquid Visual
Biodegradation, 28 days %m 55-60 % OECD 301
Potential carcinogenic label - No -
BTEX** mg/kg < 1 * ASTM 5790 mod.
PAH mg/kg < 0.1 * EPA 8100
*Below the detection level of the method.
**BTEX (Benzene, Ethylbenzene, Toluene, Xylene).

## Slide 20: Radiochemistry: drill cuttings USDOT low level radioactive waste: 2,000 pCi/g

## Slide 21: Leakage: Avoidable sources of contamination
Bank failure under liner
Fuel leak at generator
No secondary containment on drill pad

## Slide 22: Containing leaks

## Slide 23: Roll-off container leaking drill cuttings and fluid onto unlined drill pad

## Slide 24: Good: A properly constructed Impoundment

## Slide 25: Bad: Poorly installed plastic liner

## Slide 26: Unsupported pipe may break

## Slide 27: Explosions are rare but this one resulted in a major produced water release and fish kill No secondary containment

## Slide 28: Practical Risk Reduction: Polymer liner across drill pad covered with gravel. Secondary Containment around tanks

## Slide 29: Exposure Pathways A. Has not been documented B. Documented, results from poor well integrity
maybe
doubtful
A
B

## Slide 30: Most likely human/environmental exposure pathways
Shallow Aquifer
Domestic
well ~30 m
Well site spills and pit leakage
Flowback pit
Spring
Well
Pit or well site leakage could appear in a
domestic well, a spring or a stream
Casing/cement failure

## Slide 31: Recommendations: reducing accidental releases of Produced Water
Recycle/reuse flowback and produced water for frac water makeup
On site containment:
  Production casing integrity-testing prior to well completion
  Drill pad-lined and bermed
  Pits-construction/design/inspection according to State standards
  Flowback lines to be properly installed/protected
Transportation:
  Tracking and accountability
Solid waste characterization and disposal according to protective standards (RCRA)

## Slide 32: Conclusions
Produced water is highly contaminated
  Saline
  Organics (much less in dry gas wells)
  Radiochemicals
  All increase through production cycle
  Managed through recycle as makeup water
Drill cuttings toxicity controlled by drilling fluids
Exposure control via approved disposal methods
Drill cuttings radioactivity is low

## Slide 33: Salts have been declining in the Monongahela River since 2010

## Slide 34: For more information Please Contact:
Paul Ziemkiewicz
pziemkie@wvu.edu
304 293 6958